# Explorerhat
welcome.py	simple exercises
welcome-input.py	Digital inputs exercises
_tutorial_explorerhat.py	Imports _tutorial.py. doesn’t seem to do anything
test.py	This basic example tests the various functions of Explorer HAT, touching any of the buttons should output a message, lights should pulse and analog/digital values should be read every second. / #https://github.com/pimoroni/explorer-hat/blob/504720e4bee2b2c9241430832a9370251ed5bc7e/examples/test.py
test2.py	Series of lights tests. / #https://github.com/pimoroni/explorer-hat/commit/504720e4bee2b2c9241430832a9370251ed5bc7e
eventbinding.py	This example shows how you can toggle lights when a button is touched. It'll also print out the values of the digital inputs when they change, try hooking up a tactile switch! Press CTRL+C to exit.
ldr.py	This example shows how you can read the light level from an LDR connected to analog one, and turn on the onboard LEDs to indicate the measured level.
sensor.py	This is for reporting on the value of a variable resistor, the ‘sensor’. / Circuit: A voltage divider, with two resistors, R1 (fixed) and R2 (the sensor). Resistor R1: one end connected to 5V the other to Analog Input 1 and resistor R2, Resistor R2: connect the other end to GND. / The Pi measures the voltage drop V2 across R2. Using Ohm's law, one computes the resistance R2. / Possible sensors: / - a light dependent resistor / - two wires attached to two nails immersed / in a glass of water or stuck into the soil of a potted plant. / - etc, etc. / Extra. Connect the positive side of a red LED to 5V and the negative side to a 220 Ohm resistor. Connect the resistor to Output 1. Do the same with a green LED but connect its resistor to Output 2. The red LED will be on when the voltage exceeds 'threshold'. In the contrary case the green LED will be on.